PART 1 – GENERAL

1.1	SUMMARY OF PRODUCT

- Echotrol™ Techfoam Panels manufactured with open-cell, fiber-free melamine foam.

  - SUBMITTALS

- Shop Drawings: Show fabrication and installation details for acoustic round baffles, including plans, elevations, sections, details and attachment to other work.

- Submittals:  Furnish samples, showing manufacture full range of colors, texture and patterns available for each type of acoustic product specified.

- Qualification Data: For firms specified in “Quality Assurance” Article to demonstrate their capabilities and experience.

- Product Certificates: Signed by manufacturer certifying that the products furnished comply with requirements.

  - QUALITY ASSURANCE

- Manufacturer and Installer Qualifications: Manufacturer and Installer shall have a minimum of 5 years experience in producing and installing specified products and shall furnish supporting documentation showing completed jobs of approximately the same size and scope.

  - DELIVERY, STORAGE, AND HANDLING

- Protect acoustic round baffles from water, rain, and/or snow when shipping/handling.

- DO NOT drag baffles across surfaces as baffle damage/soiling can occur.

- Only install acoustic round hanging baffles when building is enclosed and HVAC is operational.

- Do not install acoustical round hanging baffles until wet work is complete and dry.

- Install baffles after painting and flooring is completed and/or installed.

PART 2 – PRODUCTS

2.1	PANELS, GENERAL

- The manufacturer’s acoustic panels shall be made with 2kg/m3 open-cell, fiber-free melamine foam.

- Product Model: Echotrol™ Techfoam Panels

Western Noise Control

T: (800) 661-7241   |   E: info@acousticsolutions.com

- Finish Materials: A Either raw (Natural White or Light Grey) OR Acoustically Transparent Factory Paint (Sherwin Williams) as per Architect

- Panel Type: Flat or Wave – Specify One.

- Panel Thickness: Nominal 1.5”, 2” or 3” – Flat Panels  |  3” Only – Wave Panels

- Noise Reduction Coefficient:  1.5”=0.8.  |  2”=1.0  |  3”=1.0

- Panel Width: Up to 1200mm (48”) - nominal size.

- Panel Length: Up to 2400mm (96”) - nominal size.

2.2	CONSTRUCTION

- The acoustic panel product shall be supplied in widths and lengths as indicated.

2.3	MOUNTING

A.	Mounting Accessories: Manufacturer’s standard accessories for securely mounting panels of type and size indicated and complying with the following requirements:

- Install materials in accordance with manufacturer's printed instructions and to comply with governing regulations, fire resistance rating requirements as indicated and industry standards applicable to the work.

- Install units after ceiling work is complete.

2.4	ACOUSTIC PERFORMANCE

Sound Absorption: Per ASTM C–423 Type A Mounting

1.5” Thick Sound Absorption Coefficient per Octave Band Center Frequency

125Hz	250Hz	500Hz	1000Hz	2000Hz	4000Hz		NRC

0.17	0.28	0.84	0.99	1.03	1.04		0.80*

2” Thick Sound Absorption Coefficient per Octave Band Center Frequency

125Hz	250Hz	500Hz	1000Hz	2000Hz	4000Hz		NRC

0.23	0.48	1.08	1.19	1.16	1.11		1.0*

3” Thick Sound Absorption Coefficient per Octave Band Center Frequency

125Hz	250Hz	500Hz	1000Hz	2000Hz	4000Hz		NRC

0.45	0.87	1.26	1.07	1.06	1.10		1.0*

*Note:	Average NRC is based on the 250,500, 1000, and 2000 Hz frequency bands and rounded to nearest multiple of 0.05.

2.5	SURFACE BURNING CHARACTERISTICS

- All components pass flame spread and smoke development tests for ASTM E84 Class A.

PART 3 – EXECUTION

  - INSTALLATION

- Install acoustic baffles in locations indicated and in alignment with other panels   Comply with manufacturer’s written instructions for installation of panels using type of mounting accessories indicated or, if not indicated, as recommended by manufacturer.

  - CLEANING

- After completion of installation of baffles, remove dust and other foreign material with a horsehair duster brush mounted on a vacuum cleaner.

END OF SECTION