PART 1 – GENERAL

1.1	SUMMARY OF PRODUCT

- HD Techfoam Acoustic Panels manufactured with water resistant, chemically resistant, and dust-free acoustic polyolefin foam containing flame retardant additives.

  - SUBMITTALS

- Shop Drawings: Show fabrication and installation details for acoustic panels, including plans, elevations, sections, details and attachment to other work.

- Submittals:  Furnish samples, showing manufacture full range of colors, texture and patterns available for each type of acoustic product specified.

- Qualification Data: For firms specified in “Quality Assurance” Article to demonstrate their capabilities and experience.

- Product Certificates: Signed by manufacturer certifying that the products furnished comply with requirements.

  - QUALITY ASSURANCE

- Manufacturer and Installer Qualifications: Manufacturer and Installer shall have a minimum of 5 years experience in producing and installing specified products and shall furnish supporting documentation showing completed jobs of approximately the same size and scope.

  - DELIVERY, STORAGE, AND HANDLING

- Protect acoustic panels from water, rain, and/or snow when shipping/handling.

PART 2 – PRODUCTS

2.1	PANELS, GENERAL

- The manufacturer’s acoustic panels made with water resistant, chemically resistant, and dust-free acoustic polyolefin foam containing flame retardant additives.

- Product Model: Echotrol™ HD Techfoam Panel

Western Noise Control

T: (800) 661-7241   |   E: info@acousticsolutions.com

- Colour: Black or White Polyolefin Foam

- Panel Thickness: Nominal 1” or 2”

- Noise Reduction Coefficient:  NRC of 0.75 for 1”, NRC of 1.0 for 2”

- Panel Width: Up to 1200 mm (48”)  - nominal size

- Panel Length: Up to 2400 mm (96”) - nominal size

2.2	CONSTRUCTION

- The acoustic panel product shall be supplied in widths and lengths as indicated.

2.3	MOUNTING

A.	Mounting Accessories: Manufacturer’s standard accessories for securely mounting panels of type and size indicated and complying with the following requirements:

- Engineered steel panel mounting plates to be securely attached to the wall substrate according to manufacturer’s specification and adhesively bonded to the back of panel.  Adhesive/Sealant is also to be applied to backside perimeter of panel.

2.4	ACOUSTIC PERFORMANCE

Sound Absorption: Per ASTM C–423 Type A Mounting

1” Thick Sound Absorption Coefficient per Octave Band Center Frequency

125Hz	250Hz	500Hz	1000Hz	2000Hz	4000Hz		NRC

0.02	0.30	.68	1.08	0.90	0.83		0.75*

2” Thick Sound Absorption Coefficient per Octave Band Center Frequency

125Hz	250Hz	500Hz	1000Hz	2000Hz	4000Hz		NRC

0.11	1.05	1.08	0.90	0.95	0.81		1.0*

*Note:	Average NRC is based on the 250,500, 1000, and 2000 Hz

frequency bands and rounded to nearest multiple of 0.05

2.5	SURFACE BURNING CHARACTERISTICS

- All components pass flame spread and smoke development tests for ASTM E84 Class 1/A (Flame Index 10, Smoke Index 30), FMVSS-302, and UL94 (HF-1).

2.6	FUNGAL RESISTANCE

- All components pass ASTM C1338-08.

2.7	WATER ABSORPTION (BY DIFFUSION)

- Water absorption is <4% in RH >95% after 28 days as per EN 12088.

PART 3 – EXECUTION

  - INSTALLATION

- Install acoustic panels in locations indicated and in alignment with other panels.   Comply with manufacturer’s written instructions for installation of panels using type of mounting accessories as recommended by manufacturer.

  - CLEANING

- After completion of installation of panels, remove dust and other foreign material with a horsehair duster brush mounted on a vacuum cleaner. A damp cloth with mild detergent and warm water or foam/pure water-free solvents can also be used for heavier soiling.

END OF SECTION