PART 1 – GENERAL

1.1	SUMMARY OF PRODUCT

- Secure Plus Metal Acoustic Panels manufactured with formaldehyde-free high density acoustic insulation that meets CGSB 51-GP-10M and is GREENGUARD Gold Certified. Intended for high security applications such as interview rooms, correctional centers, courthouses, etc.

  - SUBMITTALS

- Shop Drawings: Show fabrication and installation details for acoustic panels, including plans, elevations, sections, details and attachment to other work.

- Submittals:  Furnish samples, showing manufacture full range of colors, texture and patterns available for each type of acoustic product specified.

- Qualification Data: For firms specified in “Quality Assurance” Article to demonstrate their capabilities and experience.

- Product Certificates: Signed by manufacturer certifying that the products furnished comply with requirements.

  - QUALITY ASSURANCE

- Manufacturer and Installer Qualifications: Manufacturer and Installer shall have a minimum of 5 years experience in producing and installing specified products and shall furnish supporting documentation showing completed jobs of approximately the same size and scope.

  - DELIVERY, STORAGE, AND HANDLING

- Protect Secure Plus panels from water, rain, and/or snow when shipping/handling.

- DO NOT drag panels across surfaces as fabric/panel damage/soiling can occur.

- Only install acoustic panels when building is enclosed and HVAC is operational.

- Do not install acoustical panels until wet work is complete and dry.

- Install panels after painting and flooring is completed and/or installed.

PART 2 – PRODUCTS

2.1	PANELS, GENERAL

- The manufacturer’s acoustic panels shall be made with high density (48kg/m3//3.0 lb/ft3) formaldehyde-free smooth fiberglass.

- Product Model: Echotrol™ Secure Plus Acoustic Panel

Western Noise Control

T: (800) 661-7241   |   E: info@acousticsolutions.com

- Acoustically Transparent Heavy Duty Coated Perforated metallic face optimized for open area for NRC acoustic performance.

- Colour: Powder Coating with RAL colours

- Panel Thickness: Nominal 1” or 2”, thick panels.

- Noise Reduction Coefficient:  NRC of 0.65 for 1”, NRC of 0.95 for 2”

- Panel Width: Up to 1200 mm (48”)  - nominal size

- Panel Length: Up to 2400 mm (96”) - nominal size

2.2	CONSTRUCTION

- Secure Plus panels shall be supplied in widths, lengths and finishes as indicated.

2.3	MOUNTING

A.	Mounting Accessories: Manufacturer’s standard accessories for securely mounting panels of type and size indicated and complying with the following requirements:

- As per manufacturer with Professional Engineer’s approval and conformance to seismic conditions as necessary.

2.4	ACOUSTIC PERFORMANCE

Sound Absorption: Per ASTM C–423 Type A Mounting

1” Thick Sound Absorption Coefficient per Octave Band Center Frequency

125Hz	250Hz	500Hz	1000Hz	2000Hz	4000Hz		NRC

0.13	0.24	.56	0.83	0.92	0.98		0.65*

2” Thick Sound Absorption Coefficient per Octave Band Center Frequency

125Hz	250Hz	500Hz	1000Hz	2000Hz	4000Hz		NRC

0.33	0.67	1.07	1.07	1.03	1.06		0.95*

*Note:	Average NRC is based on the 250,500, 1000, and 2000 Hz

frequency bands and rounded to nearest multiple of 0.05

2.5	SURFACE BURNING CHARACTERISTICS

- All components pass flame spread and smoke development tests for CAN/ULC S102-M88 and/or ASTM E84 Class 1/A, NFPA 255, and/or NFPA 260 (Class 1).

PART 3 – EXECUTION

  - INSTALLATION

- Install Secure Plus in locations indicated and in orientation indicated. Comply with manufacturer’s written instructions for installation of Secure Plus using type of mounting accessories indicated by manufacturer in orientation and spacing dictated by manufacturer. Comply with the following:

- Install Secure Plus plumb, straight, and flush in proper alignment.

  - CLEANING

- After completion of installation of panels, remove dust and other foreign material with a horsehair duster brush mounted on a vacuum cleaner. A damp cloth with mild detergent and warm water or foam/pure water-free solvents can also be used for heavier soiling BUT an inconspicuous section on the side of the panel should be tested beforehand when “wetting” the panel/fabric with anything.

END OF SECTION