PART 1 – GENERAL

1.1	SUMMARY OF PRODUCT

- Echotrol™ Acoustic Woodart manufactured with formaldehyde-free high density acoustic insulation that meets CGSB 51-GP-10M and is GREENGUARD Gold Certified and Canadian Sourced Wood Slats.

1.2	SUBMITTALS

- Shop Drawings: Show fabrication and installation details for Woodart, including plans, elevations, sections, details and attachment to other work.

- Submittals: Furnish samples.

- Qualification Data: For firms specified in “Quality Assurance” Article to demonstrate their capabilities and experience.

- Product Certificates: Signed by manufacturer certifying that the products furnished comply with requirements.

1.3	QUALITY ASSURANCE

- Manufacturer and Installer Qualifications: Manufacturer and Installer shall have a minimum of 5 years experience in producing and installing specified products and shall furnish supporting documentation showing completed jobs of approximately the same size and scope.

  - DELIVERY, STORAGE AND HANDLING

- Protect Acoustic Woodart from water, rain, and/or snow when shipping/handling.

- DO NOT drag Woodart components as damage/soiling can occur.

- Only install Woodart when building is enclosed and HVAC is operational.

- Do not install Woodart until wet work is complete and dry.

- Install Woodart after painting and flooring is completed and/or installed.

PART 2 – PRODUCTS

  - WOODART, GENERAL

- The manufacturer’s Woodart system shall be made with high density (96 kg/m3//6.0 lb/ft3) formaldehyde-free smooth fiberglass faced with acoustically transparent fabric.

- Product Model: Echotrol™ Acoustic Woodart

Western Noise Control

T: (800) 661-7241   |   E: info@acousticsolutions.com

- Fiberglass Facing Materials: Acoustically Transparent Fabrics as per Architect and wood slats.

- Acoustic Core Thickness: Nominal 1” or 2”

- Noise Reduction Coefficient:  NRC of 0.8 for 1”, NRC of 1.0 for 2”

- Woodart Frame Width: Up to 2438 mm (96”).

- Woodart Frame Length: Up to 3040 mm (120”).

- Wood length beyond frame: Up to 101 mm (4”).

- Frame as per manufacturer.

- Wood Species Options: Reclaimed, maple, birch, teak, or other as specified by Architect and approved by manufacturer.

- Wood Finish:

          - Non-wet Environments: Smooth finish. Stain and lacquer as per architect.

          - Wet Environments: Smooth finish. Stain as per architect. Polyurethane based sealant as per manufacturer.

2.2 	CONSTRUCTION

- A. Acoustic Woodart product shall be supplied in widths, lengths, and finishes as indicated.

2.3 	MOUNTING

- Mounting Accessories: Manufacturer’s standard accessories for securely mounting Acoustic Woodart of type and size indicated and complying with the following requirements:

  - Walls: As per manufacturer with Professional Engineer’s approval and conformance to seismic conditions as necessary.

  - Ceilings: As per manufacturer with Professional Engineer’s approval and conformance to seismic conditions as necessary whether suspended or at ceiling level.

2.4	ACOUSTIC PERFORMANCE

Sound Absorption: Per ASTM C–423 Type A Mounting

1” Thick Sound Absorption Coefficient per Octave Band Center Frequency

125Hz	250Hz	500Hz	1000Hz	2000Hz	4000Hz		NRC

0.11	0.24	.73	1.03	1.10	0.87		0.80*

2” Thick Sound Absorption Coefficient per Octave Band Center Frequency

125Hz	250Hz	500Hz	1000Hz	2000Hz	4000Hz		NRC

0.29	0.98	1.09	0.96	1.01	0.97		1.0*

*Note:	Average NRC is based on the 250,500, 1000, and 2000 Hz

frequency bands and rounded to nearest multiple of 0.05

2.5 	SURFACE BURNING CHARACTERISTICS

- A. All components pass flame spread and smoke development tests for CAN/ULC S102-M88,

- ASTM E84 Class 1/A, NFPA 255, and/or NFPA 260 (Class 1).

PART 3 – EXECUTION

3.1 	INSTALLATION

- Install Acoustic Woodart in locations indicated and in orientation indicated. Install absorptive material into the Woodart when installation is complete or cannot be completed without absorptive material. Comply with manufacturer’s written instructions for installation of Woodart using type of mounting accessories indicated by manufacturer in orientation and spacing dictated by manufacturer. Where multiple pieces of suspended Woodart may move freely due to seismic activity, secure them together as indicated by manufacturer.

3.2 	CLEANING

- After completion of installation of Acoustic Woodart, remove dust and other foreign material with a horsehair duster brush mounted on a vacuum cleaner. A damp cloth with mild detergent and warm water or foam/pure water-free solvents can also be used for heavier soiling BUT an inconspicuous section on the side should be tested beforehand when “wetting” the Woodart with anything.

END OF SECTION